Taking 869MHz CC1101-CC1190EM boards to 915 MHz

Characterize RX/TX gain and sensitivity changes.

SmartRF setup:
Expert Mode
Base Frequency and TX Power changed according to test

–- Baseline the sensitivity and Front End gains prior to mods:

Sensitivity

Unit A (Receiver):
Range Extender: CC1190
EM Revisions: CC1101-CC1190EM 869 Mhz
1st entry under CC1101-CC1190 868MHz loaded
Freq: 870 MHz
TX Power: NA
Packet RX defaults with “Infinite” packet count checked.

Unit B (Transmitter):
Range Extender: None
1st entry under Generic 868MHz loaded
Xtal Freq: 27MHz
Freq: 870 MHz
TX Power: Variable to get sensitivity

Unit A Pre-mod characteristics:

Sensitivity:
18 dB attenuator on Rcvr input
Tx antenna replaced with two 30 dB attentuators
Packet RX defaults with “Infinite” packet count checked.
-114.9 dBm PER: 34.3% BER: 0.18%

RX Gain Reference:
Using RG-316 TBD” cable
TPI Synthesizer
18dB attenuator at RX antenna port
-53 dBm Synth for -80 dBm continuous RX

TX gain reference:
Using RG-316 TBD” cable
Gw INSTEK GSP-730 Spectrum Analyzer
15 dBm TX through 18 dB attenuator: -2.4 dBm

– Unit A SAW filter replaced with 39pF Capacitor

Removed with heat gun @900F with small circular nozzle

870 MHz:
Sensitivity: ~ -110 dBm PER: 20% BER: 0.1%
RX Gain: -67 dBm (+13 dB)
TX Gain: -6.4 dBm (-4 dB) @ 15 dBm out
        -2.4 dBm (-0 dB) @ 16 dBm out
        -1.4 @17, +1.6 @18, +3.6@19, +3.6 @20

TX drive is higher, needs a new PA table.
RX sensitivity degraded – due to no filter(?).

902 MHz:
Sensitivity: Couldn't adjust well, but less than -105 dBm
RX Gain: -68 dBm (+12 dB)
TX Gain: -4 dBm @15, -3 @16, -2 @17, 2 @18, 3 @19, 3 @20

– Unit A SAW filter replaced with 915 MHz filter

902 MHz:
Sensitivity: -115.3 dBm PER: 34.8% BER: 0.18%
RX Gain: -72 dBm (+8 dB)
TX Gain: -4@15 -3@16, -2@17, 1@18, 2@19, 3@20

– Unit A XTAL replaced with 26 MHz
EM Revisions: EM CC1101-CC1190EM 915Mhz
Base Frequency: 902 MHz

RX Gain: -72 dBm
TX Gain: